## Slide 1: Hand gesture recognition using Kinect sensor
Master Thesis
Supervisor : Dr. Truong Quang Vinh
Presented by: Nguyen Trong Tri

## Slide 2: Agenda
Introduction
Related Work
Proposed Method
Experimental Results
Conclusion
Future Research

## Slide 3: Introduction

## Slide 4: Introduction
In human-computer interaction (HCI) system, recognizing hand gestures are
more and more significant.
  an intriguing problem with many applications.

## Slide 5: Introduction
A lot of researches on hand gesture recognition from color image but they remain a challenging task due to the complex geometry of hand and difficulties in distinguishing hand from object with same color.
Depth-sensing camera (Kinect, Xtion) add a dimension, provide depth data to improve the accuracy of gesture recognition.

## Slide 6: Introduction
Kinect camera

## Slide 7: Related Work

## Slide 8: Related Work
RGB image based approaches
[1] Parul Chaudhary, Hardeep Singh Ryait, "Neural Network Based Static Sign Gesture Recognition System," International Journal of Innovative Research in Computer and Communication Engineering, February 2014.
Hand extraction: Using L*a*b color space
Hand feature extraction:
Feature vector =[area, x-centroid, y-centroid, centroid-distance, Average height]
Hand gesture classification: using Neural Network
Result: Depend on number of classification gestures

## Slide 9: Related Work
RGB image based approaches
[2] Luigi Lamberti, Francesco Camastra, “Real-Time Hand Gesture Recognition Using a Color Glove”, Springer Proceedings of the 16th international conference on Image analysis and processing, Part I ICIAP, (2011).
Hand extraction: Using HSV color space
Hand feature extraction: Nine numerical features formed
by distances from palm to all fingers and four angles between
Hand gesture classification: Learning Vector Quantization
Result: 97.79 % with 13 gestures
Notes: [1

## Slide 10: Related Work
Depth image based approaches
[4] Yi Li, “Hand gesture recognition using Kinect”, Software Engineering and Service Science (ICSESS), IEEE 3rd International Conference on, 2012.
Hand extraction: Using K-means Algorithm with Z-range = [60cm, 80cm]
Hand feature extraction: Number of fingers, finger name, angles between extended fingers and hand center
Hand gesture classification: No training. User needs to open the hand before performing a gesture. Three classifier layers: finger counting, finger name collecting, and vector matching.
[5] Yan Wen, et. al, "A Robust Method of Detecting Hand Gestures Using Depth Sensors," Haptic Audio Visual Environments and Games (HAVE), IEEE International Workshop on, 2012.
Hand Extraction: Use K-means Algorithm with Z-range = Min Depth +-10 cm
Hand Features: Number of fingers, palm center, fingertips.

## Slide 11: Related Work
RGB image based approaches
[8] Fabio Domini, et al., "Hand Gesture Recognition with Depth Data," ARTEMIS '13 Proceedings of the 4th ACM/IEEE international workshop on, pp. 9-16, 2013.
Hand extraction: Using closest point and CIELAB color space
Hand feature extraction: Distance features computed on the finger samples and Curvature features computed on the hand contour
Hand classification: Using SVM to recognize 10 gestures
Result: 99.5% with 11 gestures

## Slide 12: The Proposed Method

## Slide 13: The Proposed Method

## Slide 14: The Proposed Method
Hand Extraction
Find hand using depth image and hand point
, (mm)

## Slide 15: The Proposed Method
Hand Extraction
Reduce noise

## Slide 16: The Proposed Method
Hand Extraction
Find hand contour

## Slide 17: The Proposed Method
Hand feature extraction
Find hand orientation
The moment of order (p + q)
The major axis angle

## Slide 18: The Proposed Method
  Hand feature extraction
  Find Inscribed circle
    Minimum inner distance
    Maximum element of inner distances set

## Slide 19: The Proposed Method
Hand feature extraction
Detect fingertips: K-curvature
  Find an isosceles triangle on
  the hand contour
  ,
  Set a maximum threshold to the vertex angle
Notes: K=
V=

## Slide 20: The Proposed Method
Hand feature extraction
Feature Vector
Vf = {N, α[i], β[j], D[i]}

## Slide 21: The Proposed Method
Hand feature extraction
Feature Vector Examples

## Slide 22: The Proposed Method
Hand gesture classification
Support Vector Machine

## Slide 23: Experimental Results

## Slide 24: Experimental Results
Sampling Testing
11 gestures: referred from [8]
620 samples of 5 people for training
1926 samples of 9 people for testing

## Slide 25: Experimental Results
Sampling Testing
Confusion matrix

## Slide 26: Experimental Results
Visual Testing
Record video with10 people
Confusion matrix

## Slide 27: Experimental Results
Application Testing
HCI Application with Kinect
“Rock, paper, scissors” game

## Slide 28: Conclusion

## Slide 29: Conclusion
Input with a single depth camera
No color markers, tools are required
Independent on light condition
Real-time computation (30 fps)
Hand Feature descriptors
  Hand orientation
  Palm region
  Fingertips
High accuracy (95% with 11 gestures)

## Slide 30: Future Research

## Slide 31: Future Research
Add more gestures
Add more feature descriptor from depth and color data
Advanced machine learning strategies
Extension to dynamic gestures recognition
Extension to application on Windows
Port to ARM-LINUX for further application

## Slide 32: References
[1] Yan Wen, Chuanyan Hu, Guanghui Yu, Changbo Wang, "A Robust Method of Detecting Hand Gestures Using Depth Sensors," Haptic Audio Visual Environments and Games (HAVE), IEEE International Workshop on, 2012.
[2] Parul Chaudhary, Hardeep Singh Ryait, "Neural Network Based Static Sign Gesture Recognition System," International Journal of Innovative Research in Computer and Communication Engineering, February 2014 .
[3] Luigi Lamberti, Francesco Camastra, "Real-Time Hand Gesture Recognition using a Color Glove," Springer Proceedings of the 16th international conference on Image analysis and processing:, 2011.
[4] W.-c. Chen, "Real-Time Palm Tracking and Hand Gesture Estimation," Master Thesis, 2011.
[5] Li Yi, "Hand gesture recognition using Kinect," Software Engineering and Service Science (ICSESS), 2012 IEEE 3rd International Conference on, 2012.
[6] Raheja, J.L. , "Tracking of Fingertips and Centers of Palm Using KINECT," Computational Intelligence, Modelling and Simulation (CIMSiM), 2011 Third International Conference on, 2011.
[7] Suzuki, S. and Abe, K., , "Topological Structural Analysis of Digitized Binary Images by Border Following. CVGIP 30 1, pp 32-46," 1985.
[8] Fabio Domini, et al., "Hand Gesture Recognition with Depth Data," ARTEMIS '13 Proceedings of the 4th ACM/IEEE international workshop on, pp. 9-16, 2013

## Slide 33: Thanks for Your Attention